QUantifying flow and reactive transport in the heterogeneous subsurface environment: From pores to porous media and facies to aquifers

# Timothy D. Scheibe*

*	Pacific Northwest National Laboratory

P.O. Box 999, MS K9-36, Richland, WA 99352 USA

e-mail: tim.scheibe@pnl.gov, web page: http://subsurface.pnl.gov

Summary.  Hydrogeologists working on problems related to groundwater contamination, remediation, or water quality protection face an extraordinary challenge. The fundamental transport and reaction processes that control contaminant fate occur at length scales that are many orders of magnitude smaller than the scales at which predictions of observable phenomena are needed. Spatial variability (heterogeneity) of physical and biogeochemical properties exists across the entire range of relevant scales.

In this presentation, we will take a numerical journey through this range of length scales. Along the way, we will examine a number of case studies that illustrate both the challenges posed and some exciting ways that advanced computational methods are being brought to bear on these problems. We will start by examining pore-scale simulations of flow, transport, and reactions in porous media, in which the complex geometry of solid grains and pore spaces is explicitly quantified. Pore-scale models are being used to develop new understanding of fundamental processes that can be incorporated into larger-scale models that treat porous media as effective continua.

We will consider the applicability of two approaches: (1) direct upscaling of pore-scale simulation results using various methods, and (2) multiscale hybrid modeling, in which pore- and continuum-scale models are combined within a single simulation. At the continuum scale, complex geological heterogeneity is expressed at a multitude of scales. For example, in sedimentary aquifers one may observe sediment architectural elements such as lamination (typically millimeter scale), cross-bedding (typically centimeter scale), and larger units such as beds, bed sets, facies, formations, aquifers, and aquitards. We will examine the representation of geologic heterogeneity in reactive transport models, with a focus on the effects of correlated physical and biogeochemical heterogeneity. These issues will be presented in the context of a number of field sites relevant to U.S. Department of Energy contamination problems, including a bacterial transport site, a uranium bioremediation site, and a site with persistent uranium contamination associated with diffusion-controlled mass transfer processes.