NUMERICAL MODELING OF BEDROCK-ALLUVIAL TRANSITIONS IN RIVERS

Gary Parker

Dept. of Civil & Environmental Engineering and Dept. of Geology

University of Illinois, Urbana, IL USA

Vaughan Voller

Dept. of Civil Engineering

University of Minnesota, Minneapolis MN USA

The bed of an alluvial river is underlain by a relatively thick layer of loose sediment.  The river bed is free to degrade (downcut) into its own alluvium in response to changed conditions, such as reduced sediment supply.  A bedrock river, on the other hand, has only a discontinuous cover of alluvium over a hard material such as rock or very stiff clay/till.  Such rivers are not free to degrade over engineering/short geomorphic time.  Many rivers are bedrock-controlled in their upper reaches, but make a transition to complete alluviation in their lower reaches.  The modeling of the morphodynamics of rivers with bedrock-alluvial transitions presents several numerical challenges.  Here the problem is formulated in two ways: a) moving boundary coordinates and b) analysis with a“mushy layer” in analogy to a liquid-solid interface.  The analysis is applied to the lower Mississippi River, which is unusual in that it exhibits an alluvial-bedrock transition upstream, and then a bedrock-alluvial transition farther downstream.  In this case, the “bedrock” consists of consolidated Pleistocene clay.